## Slide 1
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Threat
Escalation Factor
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Hazard
Step 1 Identify the Hazard
Is the hazard specific? (i.e. specify location, size etc if relevant)
Has it been described in its controlled state?
Step 2 Identify the Top Event
Does it describe how control of the hazard has been lost?
Does it describe what has been lost?
Has the event been quantified (if relevant)?
Step 3 Identify Threats
Step 4 Identify Consequences
Step 5 Identify Preventative Barriers
Step 6 Identify Mitigative Barriers
Does each threat identified directly cause the Top Event?
Has it been described as [Damage] due to [Top Event]? (e.g Fire due to loss of containment)
Is it specific?
Is it capable of completely stopping the Top Event?
Does it prevent the Threat from occurring?
Step 7 Identify Escalation Factors
Does it define how or why the barrier has degraded?
Does it reduce the effectiveness of the barrier?
Is it associated with a human or organisational factor?
Is it realistic?
Is it specific?
Does it prevent or limit the consequence?
Double click on the shapes above and input descriptions to complete the elements that make up the Bowtie Diagram. The element descriptions should conform to the questions asked below.

## Slide 2
Valid Accounts Stolen from a Student
Malicious Intrusion
Remote Desktop Protocol (RDP)
Scenario 1: Gaining initial foothold in the system
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Audit the Remote Desktop Users group membership regularly.
Remove unnecessary accounts and groups from Remote Desktop Users groups.
Malicious Actions with logged in user privileges
Compromises Hosts
Secure remote access to internal PC’s and PLC’s
Secure portable media
Clean support computers
Regular patching, minimal applications, AV scan etc. for the jump server
S.No | High level RA on the identified Scope. | Mitigation measures
1 | Adversaries may use Valid Accounts(stolen from a student) to log into a computer in NTNU and e Remote Desktop Protocol (RDP). The adversary may then perform actions as the logged-on user. | Audit the Remote Desktop Users group membership regularly. Remove unnecessary accounts and groups from Remote Desktop Users groups.
4 | Initial Access consists of techniques that use various entry vectors to gain their initial foothold within the Ferry nework.(MA-OS1 and MA-OS2/Portable OS) | Establish approved support mechanism like secured remote access, secured portable media, clean support computer and secured remote access to access any internal PC and PLC's if there is any process control hardware. Jump servers should be properly controlled like Regular patching, minimal applications, AV scan etc.

## Slide 3
internal spear phishing
System Discovery and Credential Harvesting Campaign
Malicious Software
Scenario 2: Gaining sensitive information about the system
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Email Gateways
Attackers with more information about the system
Compromised Credentials
Email Gateways Monitoring tools do not usually scan internal emails
Escalation Factor
S.No | High level RA on the identified Scope. | Mitigation measures
2 | Adversaries may use internal spearphishing to gain access to additional information by controlling the NTNU's server/device with previously installed malware or by compromising the account credentials of the user. | Monitor email gateways usually do not scan internal email.

## Slide 4
Single 4G/5G link
Loss of communication
Scenario 3:
Communication failure between Ferry and RCC
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Loss of view and control of the ferry from RCC
Backup 45/5G or other communication link
RCC: Remote Control Center
S.No | High level RA on the identified Scope. | Mitigation measures
3 | Single point of failure for the Ferry any of the 4g/5G devices is down | 4G backup line

## Slide 5
Malicious Remote Access Tools
Malicious Lateral Movement
Legitimate Credentials with Native Network and Operating System Tools
Scenario 4: attackers moving through the environment
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Network Segmentation
Attackers propagate and move freely within the network
Remote Services
Strict Access Control and Management of Change (MoC) with proper Validation
S.No | High level RA on the identified Scope. | Mitigation measures
5 | The adversary is trying to move through your environment. Adversaries might install their own remote access tools to accomplish Lateral Movement or use legitimate credentials with native network and operating system tools, which may be stealthier. | Implement Vlan to segment OT devices and communication equipment like Routers, Switches
6 | Adversaries may leverage remote services to move between assets and network segments. These services are often used to allow operators to interact with systems remotely within the network, some examples are RDP, SMB, SSH, and other similar mechanisms | Strict Access control and MoC (Management of Change measures with propoer validation measures

## Slide 6
Commonly used port
(RDP, SMB, SSH, etc.)
Covert Communication Channels
Scenario 5:
Malicious Command and Control Communication in the environment
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Firewalls
Malicious control over compromised hosts
Intrusion Detection Systems
Allowed services for remote management
Escalation Factor
S.No | High level RA on the identified Scope. | Mitigation measures
7 | Adversaries may communicate over a commonly used port to bypass firewalls or network detection systems and to blend in with normal network activity, to avoid more detailed inspection. | Firewall at the NTNU terminal point and at the Ferry so that the inbound and outbound communications between the Ferry and NTNU is monitored and filtered.

## Slide 7
Repetitive Change of the I/O point values at the (Control computer)
Malicious Control Function
Scenario 6:
Attackers able to manipulate the control process function
Threat
Preventative Barrier
Mitigative Barrier
Consequence
Top Event
Network Segmentation
An undesired system state or action is reached
S.No | High level RA on the identified Scope. | Mitigation measures
8 | Adversaries may repetitively or successively change I/O point values at the (Control computer) to perform an action. Brute Force I/O may be achieved by changing either a range of I/O point values or a single point value repeatedly to manipulate a process function | LAN Segmentation btw ICS/OT equipment and IT connectivity. If there is a need to merge use devices via DMZ.